## Slide 1: Transparent Hardware Management of Stacked DRAM as Part of Memory
Jaewoong Sim Alaa R. Alameldeen Zeshan Chishti
Chris Wilkerson Hyesoon Kim
MICRO-47 | December 2014

## Slide 2: Heterogeneous Memory System
Stacked DRAM
DRAM Cache
FAST Memory
Die-stacking is happening NOW!
  Use as a large cache (DRAM$)
  Use as part of memory (PoM)
CPU
Off-Chip Memory
Data Duplication 
SLOW Memory
JEDEC: HBM & Wide I/O2 Standards
Micron: Hybrid Memory Cube (HMC)
Single Flat Address Space!
Q: How to design PoM architecture?

## Slide 3: Stacked DRAM as PoM
PoM Architecture
  Increase overall memory capacity by avoiding duplication
Static PoM
  Physical address space statically mapped to fast & slow memory
SLOW Memory
(16GB)
FAST Memory
(4GB)
0x0
0xFFFFFFFF
0x4FFFFFFFF
Need Migration
20%

## Slide 4: Stacked DRAM as PoM
Profiling
Execution
Update
Page Table/
Flush TLBs
OS-Managed PoM (Interval-Based)
Disadvantages
  Require costly monitoring hardware
  OS page (4KB, 2MB) migration granularity
  Interval should be large enough!
Application Run
Nth interval
OS Interrupt/
Handler Invocation
Page Migration
Memory Pages
HW counters for every active page
Often unable to capture
short-term hot pages!
4 fast memory slots

## Slide 5: Stacked DRAM as PoM
Potential of HW-Managed PoM
  Eliminate OS-related overhead
  Migration can happen at any time
Chart: LLC Misses Serviced from Fast Memory
| AVG.
10M | 0.32609
1M | 0.44353
100K | 0.51118
10K | 0.71768
+40%
Goal: Enable a Practical,
Hardware-Managed PoM Architecture

## Slide 6: Outline
Motivation
Hardware-Managed PoM
  Challenges
  A Practical PoM Architecture
Evaluations
Conclusion

## Slide 7: Hardware-Managed PoM
Challenges of HW-Managed PoM
Metadata for GBs of Memory!

## Slide 8: Challenges of HW-Managed PoM (1) Hardware-Managed Indirection
Requirement?
  Relocates memory pages in an OS-transparent manner
Challenge 1: Maintain the integrity of OS’s view of memory
  Approach 1: OS page table modification via hardware (unattractive)
  Approach 2: Additional indirection by remapping table
Remapping Table (2GB Stacked DRAM/2KB Segment)
  Size: tens of MBs
  Latency: tens of cycles
Page Table Physical Address (PTPA)
DRAM Physical Address (DPA)
PA Remapping
Where to architect this? 
Added to every memory request  
Our Approach: Two-Level Indirection with Remapping Cache
Remapping granularity!

## Slide 9: Challenges of HW-Managed PoM (2) Efficient Memory Activity Tracking/Replacement
Challenge 2:
Provide efficient memory-usage monitoring/replacement mechanisms
Activity Tracking Structure (8GB total memory/4KB page)
  Track as many as 2M entries
  Compare/sort counters (non-trivial)
Memory Pages
P1
P2
P5
P6
P3
P4
P7
P8
P9
P10
P13
P14
P11
P12
P15
P16
Counters
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
2
1
7
87
42
27
97
4
887
124
483
63
72
38
56
7
628
2
Our Approach: Competing Counter-Based Tracking and Replacement
MBs of storage for counters
unresponsive decision

## Slide 10: Hardware-Managed PoM
A Practical PoM Architecture
(1) Two-Level Indirection

## Slide 11: A Practical PoM Architecture
Conventional System
PoM System
Virtual Address (VA)
Page Table Physical Address (PTPA)
Page
Table
VA
Page Table
Physical
Address
(PTPA)
Page
Table (OS)
DRAM
Physical
Address
(DPA)
Segment
Remapping Table (HW)
Access DRAM
Actual address of the data in memory
Remapping PTPA

## Slide 12: A Practical PoM Architecture
PoM System
VA
Page Table
Physical
Address
(PTPA)
Page
Table (OS)
DRAM
Physical
Address
(DPA)
Segment 0
Entry 0
Segment N+27
Entry 1
Entry N-1
Segment N-1
…
Originally mapped
to slow memory
Segment Remapping Table (SRT)
SRC
Processor Die
C
C
C
C
C
C
C
C
PTPA
Slow Memory
SRT
SRC Miss
DATA
Request for “Segment N+27”
DPA
Fast
Segment Remapping Cache (SRC)
Segment
Remapping Table (HW)
Cache Entry1

## Slide 13: Segment-Restricted Remapping
Can we simply cache some entries?
The remapping information can be anywhere in the SRT!
Segment 0
Entry 0
Segment N+27
Entry 1
Entry N-1
Segment N-1
…
Segment Remapping Table (SRT)
Segment 0
Entry 0
Segment 1
Entry 1
Entry N-1
Segment N+27
…
2 look-ups
N look-ups!!
A single SRC miss may require lots of memory accesses to fast memory!

## Slide 14: Segment-Restricted Remapping
How to minimize SRC miss cost?
For an SRC miss
  Segment A,C,Y -> Look up in Entry 0
  Segment B,D,Z -> Look up in Entry 1
Entry 0
SEG A
SEG C
Entry 1
SEG B
SEG D
SEG Y
SEG Z
…
Allowed to be mapped
to certain slots!
Segment-restricted remapping minimizes
the SRC miss cost to a single FAST DRAM access

## Slide 15: Hardware-Managed PoM
A Practical PoM Architecture
(2) Memory Activity Tracking and Replacement

## Slide 16: Competing Counter
How to compare counters of all involved segments?
  Information of interest is the access count relative to each segment rather than the absolute one!
Simple Case: One slot exists in fast memory
SEG A
Segments in
Fast Memory
Segments in
Slow Memory
SEG Y
SEG Y
SEG A
Counter
--
++
Can easily figure that which segment is worth for FAST memory
Memory Pages
P1
P2
P5
P6
P3
P4
P7
P8
P9
P10
P13
P14
P11
P12
P15
P16
Counters
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
2
1
7
87
42
27
97
4
887
124
483
63
72
38
56
7
628
2

## Slide 17: Competing Counter
How to compare counter of all involved segments?
General Case
SEG A
SEG C
SEG B
SEG D
Segments in
Fast Memory
Segments in
Slow Memory
SEG Y
SEG Z
C1
SEG Y
SEG A
--
++
C3
SEG Y
SEG C
--
++
C2
SEG Z
SEG B
++
--
C4
SEG Z
SEG D
++
--
Segment-Restricted Remapping
C1
SEG Y
SEG A
--
++
SEG C
++
C2
SEG Z
SEG B
++
--
SEG D
++
#Counters is bounded to #segments in slow memory!
Sharing Counter
Among Competing Segments!
#Counters is bounded to #segments in fast memory!

## Slide 18: More discussions in the paper!
Two-Level Indirection
Competing Counters
Swapping Operation
  Fast Swap and Slow Swap => affects remapping table size
Segment Remapping Table/Cache
  How to design this
Swapping Criteria
  How to determine the threshold for different applications

## Slide 19
Evaluations

## Slide 20: Methodology
System Parameters
CPU | 
Core SRC | 4 cores, 3.2GHz OOO 4-way, 32KB, LRU policy
Die-Stacked DRAM | 
Bus Frequency Ch/Rank/Bank tCAS-tRCD-tRP | 1.6GHz (DDR 3.2GHz), 128 bits per channel 4/1/8, 2KB row buffer 8-8-8
Off-chip DRAM | 
Bus Frequency Ch/Rank/Bank tCAS-tRCD-tRP | 800MHz (DDR 1.6GHz), 64 bits per channel 2/1/8, 16KB row buffer 11-11-11
Workloads
14 workloads
(a multi-programmed mix of SPEC06)
Swapping Parameters
Granularity: 2KB Segment
Latency: 1.2K CPU cycles

## Slide 21: Performance
Chart: Speedup over no stacked DRAM
| WL-1 | WL-2 | WL-3 | WL-4 | WL-5 | WL-6 | WL-7 | WL-8 | WL-9 | WL-10 | WL-11 | WL-12 | WL-13 | WL-14 | AVG.
Static (1:8) | 1.0462 | 1.0772 | 1.1071 | 1.0477 | 1.0459 | 1.0523 | 1.0134 | 1.188 | 1.048 | 1.0805 | 1.053 | 1.2103 | 1.0119 | 1.0841 | 1.0747
OS-Managed | 1.3656 | 1.0868 | 1.2324 | 1.0941 | 1.114 | 1.1251 | 0.86037 | 0.90061 | 1.0105 | 1.0747 | 1.3374 | 1.1268 | 1.0241 | 1.0625 | 1.0927
OS-Managed (zero-cost swap) | 1.4 | 1.1649 | 1.25 | 1.1005 | 1.2324 | 1.1977 | 1.0045 | 1.124 | 1.0631 | 1.1669 | 1.3851 | 1.2225 | 1.1786 | 1.2523 | 1.1913
INT_10M (Ideal)
Proposed | 1.3385 | 1.1965 | 1.75 | 1.0553 | 1.3792 | 1.3314 | 1.1024 | 1.872 | 1.003 | 1.3441 | 1.4047 | 1.1858 | 1.3393 | 1.3964 | 1.3167
No migration
7.5%
100M cycles interval
100M cycles interval
ignore migration cost
19.1%
HW-managed PoM
migration cost included
31.6%

## Slide 22: SRC: Address Translation Breakdown
Chart: 
| WL-1 | WL-2 | WL-3 | WL-4 | WL-5 | WL-6 | WL-7 | WL-8 | WL-9 | WL-10 | WL-11 | WL-12 | WL-13 | WL-14
HIT_FAST | 7756744 | 7481926 | 11349898 | 887978 | 14745112 | 13230324 | 12763187 | 38502222 | 546177 | 13366380 | 13358716 | 3081844 | 19944738 | 22304537
HIT_SLOW | 2770452 | 2317789 | 708492 | 4489537 | 853737 | 1994030 | 8547496 | 3833949 | 11029812 | 520949 | 1085011 | 15672252 | 2284348 | 2301871
MISS_FAST | 1772974 | 160706 | 69193 | 340946 | 102946 | 226151 | 93062 | 268812 | 84895 | 107975 | 514359 | 22072 | 311567 | 205401
MISS_SLOW | 1215946 | 152554 | 73623 | 1685676 | 89851 | 225034 | 249203 | 185904 | 825913 | 51748 | 99524 | 172178 | 289224 | 131832
AVG +95% SRC hit rate!!
HIT/MISS : SRC hit or miss
FAST/SLOW: Serviced from FAST or SLOW memory

## Slide 23
Conclusion

## Slide 24: Conclusion
Goal: Enable a practical, hardware-managed PoM
  Challenge 1: Maintaining large indirection table
  Challenge 2: Providing efficient memory activity tracking/replacement
Solution
  Two-Level indirection with remapping cache
    Segment-restricted remapping
  Competing Counter-based tracking/swapping
Result: A practical, hardware-managed PoM
  18.4% faster over static mapping
  With very little additional on-chip SRAM storage overhead
    7.8% of SRAM LLC